## Slide 1: L
A brain-principled chip that keeps learning after it ships
L Lawliet | Navin (Kakashi), CKCET | PALS innoWAH! 2026-27
Every number is labelled SIMULATED, ESTIMATED or MEASURED. The chip has not run on hardware yet: say it first, then show what is verified.
Notes: Hello judges. We are L Lawliet from CKCET and the project is called L. L is a small chip design that keeps learning after it ships, without forgetting what it knew, with no multiplier, no matrices and no backpropagation. One promise before the numbers: every number on these slides is labelled simulated, estimated or measured, and nothing has run on a real board yet.

## Slide 2: AI stops learning the day it ships
19.5%
digits: a small CNN that learns in 5 stages keeps only the last stage
20.0%
clothing: same test, 60,000 images, same forgetting
5.0%
20 classes in 10 stages: almost everything is forgotten
MEASURED: a CNN we trained on the same images, one seed. Fixing forgetting today means retraining from scratch: more energy, more heat, hardware thrown away when it can no longer be updated.
Notes: A normal neural network learns once. Teach it in stages and it keeps only the last stage: about 20 percent on digits and clothing, and 5 percent on twenty classes. Those are measured numbers from a small CNN we trained on the same images, one seed. The usual fix is to retrain from scratch, which costs energy and means hardware cannot be updated in the field. A chip that learns in the field avoids that.

## Slide 3: The idea: a brain, as a chip
1
Senses
Eyes and ears turn pixels and sound into a sparse code. Detectors learn by themselves, no labels.
2
Learn by counting
Each example is counted into a small fast table. No backpropagation, no multiplier, no matrices.
3
Dream and sleep
Old classes are replayed from 10-bit counters, so nothing is stored. A slow table consolidates the fast one.
4
Look again
When unsure, a second look at a finer code; when two senses disagree, trust the more confident one.
5
Share
A second chip takes over the memory, or two memories merge by adding counts.
Notes: Our rule is to follow the brain, not the GPU. Senses that learn without labels. Learning by counting, one example at a time, with no backpropagation, no multiplier and no matrices. Sleep: the chip dreams old classes from small counters instead of storing examples, and a slow table consolidates the fast one. Looking again when unsure, and trusting the more confident sense. And sharing: memory is counts, so chips can merge.

## Slide 4: It learns in stages and keeps what it knew
Chart: Accuracy after learning in stages (%)
| digits | clothing | 20 classes
L chip design (no stored examples) | 95.6 | 81 | 87.4
CNN in stages (MEASURED) | 19.5 | 20 | 5
SIMULATED (chip), MEASURED (CNN)
Exact integer model of the chip, 2-5 seeds, the full test sets. Digits and clothing: 60,000 training images in 5 stages of 2 classes. 20 classes: digits plus clothing in 10 stages.
Stored examples: none. Memory: 84 KB for images.
Notes: This is the core result. Learning in stages of two classes with no stored examples, the chip keeps 95.6 percent on digits and 81 on clothing with sixty thousand training images, and 87.4 percent on twenty classes. The CNN that learned in the same stages keeps about 20 and 5 percent. The chip numbers are simulated with an exact integer model, two to five seeds; the CNN numbers are measured, one seed.

## Slide 5: Close to a CNN trained on everything
Chart: Accuracy (%)
| digits | clothing | 20 classes | 35 words
L chip design | 98.45 | 88.93 | 91.18 | 72.4
CNN, all data at once (MEASURED) | 98.87 | 90.96 | 90.96 | 72.5
SIMULATED vs MEASURED
One pass with a second look on a finer code (digits, clothing: 60,000 images). 20 classes: one pass, no second look. Words: the chip learned in stages and the CNN all at once.
A trained CNN is still ahead on clothing by 2 points.
Notes: With everything available at once, the chip with its second look is within half a point of a trained CNN on digits, two points behind on clothing, level on twenty classes, and level on thirty-five spoken words even though the chip learned the words in stages. The second look costs about 2.8 times the table memory. Say it plainly: a CNN is still ahead on clothing.

## Slide 6: It scales: more data does not break it
Chart: Clothing in stages, by training images (%)
| 10,000 | 30,000 | 60,000
Fixed consolidation (first design) | 83.3 | 79.4 | 78
Consolidation scaled with the stage size | 83.3 | 81.2 | 81
SIMULATED, 3 seeds
We tested 6x more data and found the staged result fell. One fixed rule fixed it: follow the slow table every max(100, stage size / 30) examples. Digits: 93.4 to 95.6 at 60,000 images.
One pass barely improves with more data (clothing 86.6 to 87.6).
Notes: We tested whether the chip holds up with more data, and found a failure: at sixty thousand images the staged result fell. The cause was consolidation timing; one fixed rule that scales the follow interval with the stage size removes the collapse, on both datasets, without a per-dataset setting. We also report that one-pass accuracy barely improves with more data.

## Slide 7: It hears, and noise stops hurting as much
Chart: 35 spoken words, learned in stages, white noise (%)
| clean | 20 dB | 10 dB | 5 dB
First design | 68.3 | 56.5 | 39.8 | 27.4
Noisy copies + second look | 72.4 | 67.3 | 57.6 | 47.2
SIMULATED, 3 seeds
Raw sound to word through an integer cochlea, noise floor, word alignment and the same counting table, bit-exact in RTL. Training also on one noisy copy of each clip adds no memory.
Sound needs 422 KB: an ASIC or external memory, not the Tang Nano.
Notes: The sound path goes from raw samples through a cochlea and noise floor to the same counting table. With one noisy copy of each training clip and a second look, thirty-five words in stages reach 72.4 percent clean and 47 percent at 5 decibels, against 68 and 27 for the first design. The noise is simulated white noise, not real recordings.

## Slide 8: Two senses help each other
Chart: Digits: picture + sound (%)
| clean | picture 25% damaged | picture 50% damaged
Joint table | 98.3 | 97.5 | 94.6
Weighted by confidence | 98.9 | 98.4 | 96.2
SIMULATED, 2-3 seeds
The ear names pictures with no picture labels: 93.9 after sleep cleaning
Groups form with no labels: 96.1 to 97.0 with 30 names
New classes noticed from inside: 99% of flagged pairs are new
Pictures and sounds are paired by class, not real recordings of one scene.
Notes: A retina and a cochlea feed one table. When a quarter of the picture is damaged, weighting each sense by how confident it is lifts digits from 97.5 to 98.4. A heard word can name pictures with no picture labels, groups can form with no labels, and the chip can notice a new class by itself. Be honest: the pictures and sounds come from different datasets that share only the digit.

## Slide 9: A new class from one example, after shipping
Chart: Accuracy on all 10 classes, 1 example per new class (%)
| digits | clothing | spoken words
Before the fix | 54.1 | 49.7 | 45.2
With IMPRINT + short sleep | 69.9 | 64 | 48.3
SIMULATED, in RTL
A novelty-gated imprint writes the new class into the table at once, then a short sleep blends it in. Old classes stay within 1 to 5 points.
Spoken words from 1 to 5 recordings stay weak.
Notes: A brand-new class seen once was almost invisible. IMPRINT writes its mean code into the table at once and a short sleep blends it in: digits go from 54 to 70, clothing from 50 to 64. Spoken words from one to five recordings stay weak and I say so on the limits slide.

## Slide 10: Knowledge moves between chips
Chart: Accuracy after moving knowledge (%)
| digits | clothing | spoken words
Merge two chips | 93.3 | 81.4 | 64.3
Hand-over, then learn on | 95.6 | 82.7 | 71.6
SIMULATED, 3 seeds
Because memory is counts, two chips that learned different classes merge by adding counters. No retraining on a server. The board demo design reached 91.4% on all ten digits after one night (PC-side emulator).
Notes: Because the memory is counts, two chips that learned different classes can be merged by adding their counters, or one chip hands its memory to another that keeps learning. Merge gives 93, 81 and 64 percent; hand-over gives 96, 83 and 72. This is weight transfer without a server.

## Slide 11: Small, cheap, and no multiplier
84 KB
memory for images (second look: about 2.8x)
design fact
0
hardware multipliers on the $25 Tang Nano 20K (89% logic, 46/46 block RAM)
SIMULATED, place and route
~74x
less energy per decision than an 8-bit network, counting the operations needed (9.4 nJ vs 696 nJ)
ESTIMATED
422 KB
sound memory: needs external memory or an ASIC
design fact
Say it carefully: the 74x is per operation needed. The SKY130 layout estimate is 0.18 to 0.26 uJ per decision, 20 to 28x above the operation count.
Notes: Cost. The image memory is 84 kilobytes and fits a 25-dollar Tang Nano 20K with no hardware multipliers. Counting only the operations a decision needs it uses about 74 times less energy than an 8-bit network, an estimate. The layout estimate is higher, about a fifth of a microjoule. The second look costs about 2.8 times the table memory, and sound needs 422 kilobytes.

## Slide 12: Verified bit for bit, and laid out
38 / 38
RTL checks, 0 mismatches against the integer model: core, tail memory, IMPRINT, slow table, encoders, cochlea, sound chain, two-sense chip, cue weighting, second look, threshold and novelty units, clustering, board top, host schedule.
SIMULATED (RTL simulation)
1
violation left in detailed routing of the SKY130 layout (from 174,309 on the first pass), a power-versus-signal short at a memory macro edge.
ESTIMATED (open-source flow, no sign-off)
Notes: The design is not just a simulator result. Every check passes bit for bit between the integer model and the RTL, covering the learning core, the sense layers, the whole sound chain, the two-sense chip, the new units that moved host steps onto the chip, and the board top. We also took it through an open-source SKY130 layout flow; routing ended at one remaining violation. This is verification in simulation, not a chip.

## Slide 13: Where it is level, and where it is weaker
Nothing is measured on hardware yet: every chip number is simulated
Staged clothing about 82%, 5 points below its one pass; many ideas tried
A trained CNN is ahead by about 2 points on clothing when all data is available
Small tests: digits, clothing, 20 classes, up to 35 words; noise is simulated; two-sense data is paired by class
Second look costs about 2.8x memory; a few steps still run on the host
Notes: This is the slide I want you to remember. Nothing has run on hardware. Staged clothing is about 82 percent, five points under its one-pass number, and I tried many fixes. A trained CNN is still ahead on clothing by about two points. The tests are small and the noise is simulated; the two-sense data is paired by class, not real audio-visual recordings. The second look costs about 2.8 times the memory, and a few steps still run on the host.

## Slide 14: Not the first, and clear about what is new
Already exists
Hyperdimensional-computing accelerators
Intel Loihi 2, TrueNorth, SpiNNaker (event-driven spiking chips)
Replay-based continual learning
What we add
Dreams from 10-bit counters, no stored examples
A night that ends by itself; consolidation that scales with the data
No multiplier or matrix, bit-exact from raw senses to decision, with grouping and thresholds on the chip
Notes: We are not the first continual-learning chip. Hyperdimensional-computing accelerators and event-driven spiking chips such as Loihi 2, TrueNorth and SpiNNaker exist. What we add is the combination: dreams from small counters so no examples are stored, a night that ends by itself, consolidation that scales with the data, and a design with no multiplier or matrix that is bit-exact from raw senses to the decision.

## Slide 15: What comes next
1
Done
Model, RTL with every check passing, second look, tail memory, on-chip thresholds and grouping, scale tests
2
Next
Run on the real Tang Nano: the first MEASURED numbers
3
Then
Harder tests: larger vocabulary, real recorded noise, a harder image set
4
Later
Matrix-free chip for the L language model; ASIC memory for sound and the second look
Horizon: a provable result within 6 to 8 months, then shrink and attract investors. No fabrication is planned yet.
Notes: What comes next. The model and RTL are done and verified in simulation. The next milestone is the real Tang Nano board, which gives the first measured numbers. Then harder tests: a larger vocabulary, real recorded noise and a harder image set. Later, a matrix-free chip for the L language model, and external memory for sound and the second look. No fabrication is planned yet.

## Slide 16: A chip that keeps learning
It learns in the field, keeps what it knew, shares what it learned, and needs no multiplier. It is weaker than a trained network in some places, and we have said where.
Thank you. Questions?
Notes: To close: L is a chip design that keeps learning after it ships. It keeps what it knew, shares what it learned, and needs no multiplier. It is weaker than a trained network in a few places, and I have told you where. Thank you, I am happy to take questions.