## Slide 1: L
A brain-principled chip that keeps learning after it ships
L Lawliet | Navin (Kakashi), CKCET | PALS innoWAH! 2026-27
Every number is labelled SIMULATED, ESTIMATED or MEASURED. The chip has not run on hardware yet: say it first, then show what is verified.
Notes: Hello judges. We are L Lawliet from CKCET and the project is called L. L is a small chip design that keeps learning after it ships, without forgetting what it knew, with no multiplier, no matrices and no backpropagation. One promise before the numbers: every number on these slides is labelled simulated, estimated or measured, and nothing has run on a real board yet.

## Slide 2: AI stops learning the day it ships
19.5%
digits: a small CNN that learns in 5 stages keeps only the last stage
20.0%
clothing: same test, 60,000 images, same forgetting
5.0%
20 classes in 10 stages: almost everything is forgotten
MEASURED: a CNN we trained on the same images, one seed. Fixing forgetting today means retraining from scratch: more energy, more heat, hardware thrown away when it can no longer be updated.
Notes: A normal neural network learns once. Teach it in stages and it keeps only the last stage: about 20 percent on digits and clothing, and 5 percent on twenty classes. Those are measured numbers from a small CNN we trained on the same images, one seed. The usual fix is to retrain from scratch, which costs energy and means hardware cannot be updated in the field. A chip that learns in the field avoids that.

## Slide 3: The idea: a brain, as a chip
1
Senses
Eyes and ears turn pixels and sound into a sparse code. Detectors learn by themselves, no labels.
2
Learn by counting
Each example is counted into a small fast table. No backpropagation, no multiplier, no matrices.
3
Dream and sleep
Old classes are replayed from 10-bit counters, so nothing is stored. A slow table consolidates the fast one.
4
Look again
When unsure, a second look at a finer code; when two senses disagree, trust the more confident one.
5
Share (optional)
One chip works alone. Two chips can merge what they learned by adding counts, or one hands its memory to the other. A normal network cannot do this.
Notes: Our rule is to follow the brain, not the GPU. Senses that learn without labels. Learning by counting, one example at a time, with no backpropagation, no multiplier and no matrices. Sleep: the chip dreams old classes from small counters instead of storing examples, and a slow table consolidates the fast one. Looking again when unsure, and trusting the more confident sense. And sharing: memory is counts, so chips can merge.

## Slide 4: It learns in stages and keeps what it knew
Chart: Accuracy after learning in stages (%)
| digits | clothing | 20 classes
L chip design (no stored examples) | 95.6 | 81 | 87.4
CNN in stages (MEASURED) | 19.5 | 20 | 5
SIMULATED (chip), MEASURED (CNN)
Exact integer model of the chip, 2-5 seeds, the full test sets. Digits and clothing: 60,000 training images in 5 stages of 2 classes. 20 classes: digits plus clothing in 10 stages.
Stored examples: none. Memory: 84 KB for images.
Notes: This is the core result. Learning in stages of two classes with no stored examples, the chip keeps 95.6 percent on digits and 81 on clothing with sixty thousand training images, and 87.4 percent on twenty classes. The CNN that learned in the same stages keeps about 20 and 5 percent. The chip numbers are simulated with an exact integer model, two to five seeds; the CNN numbers are measured, one seed.

## Slide 5: Close to a CNN trained on everything
Chart: Accuracy (%)
| digits | clothing | 20 classes | 35 words
L chip design | 98.45 | 88.93 | 91.18 | 72.4
CNN, all data at once (MEASURED) | 98.87 | 90.96 | 90.96 | 72.5
SIMULATED vs MEASURED
One pass with a second look on a finer code (digits, clothing: 60,000 images). 20 classes: one pass, no second look. Words: the chip learned in stages and the CNN all at once.
A trained CNN is still ahead on clothing by 2 points.
Notes: With everything available at once, the chip with its second look is within half a point of a trained CNN on digits, two points behind on clothing, level on twenty classes, and level on thirty-five spoken words even though the chip learned the words in stages. The second look costs about 2.8 times the table memory. Say it plainly: a CNN is still ahead on clothing.

## Slide 6: It scales: more data does not break it
Chart: Clothing in stages, by training images (%)
| 10,000 | 30,000 | 60,000
Fixed consolidation (first design) | 83.3 | 79.4 | 78
Consolidation scaled with the stage size | 83.3 | 81.2 | 81
SIMULATED, 3 seeds
We tested 6x more data and found the staged result fell. One fixed rule fixed it: follow the slow table every max(100, stage size / 30) examples. Digits: 93.4 to 95.6 at 60,000 images.
One pass barely improves with more data (clothing 86.6 to 87.6).
Notes: We tested whether the chip holds up with more data, and found a failure: at sixty thousand images the staged result fell. The cause was consolidation timing; one fixed rule that scales the follow interval with the stage size removes the collapse, on both datasets, without a per-dataset setting. We also report that one-pass accuracy barely improves with more data.

## Slide 7: It hears, and noise stops hurting as much
Chart: 35 spoken words, learned in stages, white noise (%)
| clean | 20 dB | 10 dB | 5 dB
First design | 68.3 | 56.5 | 39.8 | 27.4
Noisy copies + second look | 72.4 | 67.3 | 57.6 | 47.2
SIMULATED, 3 seeds
Raw sound to word through an integer cochlea, noise floor, word alignment and the same counting table, bit-exact in RTL. Training also on one noisy copy of each clip adds no memory.
Sound needs 422 KB: an ASIC or external memory, not the Tang Nano.
Notes: The sound path goes from raw samples through a cochlea and noise floor to the same counting table. With one noisy copy of each training clip and a second look, thirty-five words in stages reach 72.4 percent clean and 47 percent at 5 decibels, against 68 and 27 for the first design. The noise is simulated white noise, not real recordings.

## Slide 8: Two senses help each other
Chart: Digits: picture + sound (%)
| clean | picture 25% damaged | picture 50% damaged
Joint table | 98.3 | 97.5 | 94.6
Weighted by confidence | 98.9 | 98.4 | 96.2
SIMULATED, 2-3 seeds
The ear names pictures with no picture labels: 93.9 after sleep cleaning
Groups form with no labels: 96.1 to 97.0 with 30 names
New classes noticed from inside: 99% of flagged pairs are new
Pictures and sounds are paired by class, not real recordings of one scene.
Notes: A retina and a cochlea feed one table. When a quarter of the picture is damaged, weighting each sense by how confident it is lifts digits from 97.5 to 98.4. A heard word can name pictures with no picture labels, groups can form with no labels, and the chip can notice a new class by itself. Be honest: the pictures and sounds come from different datasets that share only the digit.

## Slide 9: A new class from one example, after shipping
Chart: Accuracy on all 10 classes, 1 example per new class (%)
| digits | clothing | spoken words
Before the fix | 54.1 | 49.7 | 45.2
With IMPRINT + short sleep | 69.9 | 64 | 48.3
SIMULATED, in RTL
A novelty-gated imprint writes the new class into the table at once, then a short sleep blends it in. Old classes stay within 1 to 5 points.
Spoken words from 1 to 5 recordings stay weak.
Notes: A brand-new class seen once was almost invisible. IMPRINT writes its mean code into the table at once and a short sleep blends it in: digits go from 54 to 70, clothing from 50 to 64. Spoken words from one to five recordings stay weak and I say so on the limits slide.

## Slide 10: Two chips can share what they learned
Chart: Accuracy after moving knowledge (%)
| digits | clothing | spoken words
Merge two chips | 93.3 | 81.4 | 64.3
Hand-over, then learn on | 95.6 | 82.7 | 71.6
SIMULATED, 3 seeds
One chip works alone; this is an option. Because memory is counts, two chips that learned different classes merge by adding counters, with no retraining. A trained network cannot merge this way. The board demo design reached 91.4% on all ten digits after one night (PC-side emulator).
Notes: One chip works alone; sharing is an option. Because the memory is counts, two chips that learned different classes can be merged by adding their counters, or one chip hands its memory to another that keeps learning. Merge gives 93, 81 and 64 percent; hand-over gives 96, 83 and 72. A normal network cannot merge two separately trained copies like this. A GPU cluster joins many GPUs for size and speed, which is a different thing.

## Slide 11: Small, cheap, and no multiplier
84 KB
memory for images (second look: about 2.8x)
design fact
0
hardware multipliers on the $25 Tang Nano 20K (89% logic, 46/46 block RAM)
SIMULATED, place and route
~74x
less energy per decision than an 8-bit network, counting the operations needed (9.4 nJ vs 696 nJ)
ESTIMATED
422 KB
sound memory: needs external memory or an ASIC
design fact
Say it carefully: the 74x is per operation needed. The SKY130 layout estimate is 0.18 to 0.26 uJ per decision, 20 to 28x above the operation count.
Notes: Cost. The image memory is 84 kilobytes and fits a 25-dollar Tang Nano 20K with no hardware multipliers. Counting only the operations a decision needs it uses about 74 times less energy than an 8-bit network, an estimate. The layout estimate is higher, about a fifth of a microjoule. The second look costs about 2.8 times the table memory, and sound needs 422 kilobytes.

## Slide 12: Why this is an embedded system
Built for tight limits
84 KB of memory for images
No multiplier: counts, compares, shifts
Fits a Rs 4,000 FPGA (89% logic, 0 multipliers, SIMULATED place and route)
Real device interfaces
Camera-style 28x28 picture and 16 kHz microphone samples, encoded on the chip
UART byte protocol to any microcontroller or PC: learn, dream, predict, read and write memory
The board's top-level design was simulated end to end: digits recognised from UART bytes
Behaviour a device needs
Learns new classes in the field, no server
Sleeps when idle; the night ends by itself
Memory moves between devices by adding counts
Not measured yet: real power, latency and clock speed. They need the board run. Everything here is a design and simulation result.
Notes: Why this belongs with embedded systems. It is a dedicated function inside a device under tight limits: 84 kilobytes of memory for images, no multiplier, a small low-cost FPGA. It has real device interfaces: a camera-style picture input and microphone samples encoded on the chip, and a UART byte protocol so any microcontroller or PC can teach it, ask it, and read or write its memory. We simulated the board's top-level design end to end: digits recognised from UART bytes. On the device it learns new classes in the field, sleeps when idle, and its memory can be moved between devices. The honest limit: real power, latency and clock speed are not measured yet; they need the board run.

## Slide 13: Verified bit for bit, and laid out
38 / 38
RTL checks in one full run, 0 mismatches against the integer model: core, tail memory, IMPRINT, slow table, encoders, cochlea, sound chain, two-sense chip, cue weighting, second look, threshold and novelty units, clustering, board top, host schedule. Newer checks pass on their own: stage and night sequencer, raw senses to a whole stage.
SIMULATED (RTL simulation)
1
violation left in detailed routing of the SKY130 layout (from 174,309 on the first pass), a power-versus-signal short at a memory macro edge.
ESTIMATED (open-source flow, no sign-off)
Notes: The design is not just a simulator result. Every check passes bit for bit between the integer model and the RTL, covering the learning core, the sense layers, the whole sound chain, the two-sense chip, the new units that moved host steps onto the chip, and the board top. We also took it through an open-source SKY130 layout flow; routing ended at one remaining violation. This is verification in simulation, not a chip.

## Slide 14: The design, so you can verify it
Retina (picture)
Cochlea (sound)
Detectors: sparse code, learned without labels
Core: fast 5-bit table, dream counters (10-bit), slow table; counts, compares, shifts; no multiplier
Decision (XNOR + popcount)
Second look (finer code)
Tail memory (sleep)
Cue weighting (2 senses)
Thresholds, novelty, grouping
On-chip units added after the core, each checked bit for bit
Verify: every unit has a Verilog file, a testbench and a script that compares the RTL with the integer model (0 mismatches). One command, sh hw/run_all_checks.sh, reruns all checks. The repository and all logs are available to reviewers on request. Everything shown is SIMULATED; nothing is measured on hardware yet.
Notes: This is the design, so you can check it. Pictures and sound go through detectors that learn without labels and make a sparse code. The core is a fast five-bit table, ten-bit dream counters for sleep and a slow consolidating table, using counts, compares and shifts, with no multiplier. The decision is an XNOR and popcount. On top are the units we added: the second look, the tail memory, the confidence weighting of two senses, and the threshold, novelty and grouping units. Each has a Verilog file, a testbench and a script that compares it bit for bit with the integer model. One command reruns every check. The repository and logs are available to reviewers on request. Everything is simulated.

## Slide 15: What L solves, and what it does not
What L solves
Small AI on devices that must keep learning: no retraining on a server, no hardware thrown away to update it (SIMULATED)
No stored examples, 84 KB of memory for images, no multiplier
About 74x less energy per decision than an 8-bit network, counting operations needed (ESTIMATED)
What L does not solve
The cost of large language models and image generators: GPU and memory prices, data-centre heat and water
It cannot run existing models (CNNs, transformers, LLMs): it is a dedicated chip for its own brain-style model
Nothing is measured on hardware yet
Notes: Be clear about scope. L solves a small part of the AI problem: devices that must keep learning in the field without retraining on a server and without being thrown away. That is simulated, and the energy figure is an estimate. L does not solve what is driving GPU and memory prices today, which is large language models and image generators in data centres. It also cannot run existing models: it is a dedicated chip for its own model. And nothing is measured on hardware yet.

## Slide 16: The hypothesis we will test
HYPOTHESIS (not a result)
A brain-style model with constant-size state, sparse event-driven activity and low-bit weights, on a chip built for it, needs far less memory traffic and energy per token than a transformer on a GPU at the same quality, and so less scarce HBM, heat and water.
Why the model comes first
The savings come from the model's state size, sparsity and low-bit weights. A chip can only exploit them, not create them. L Cortex proves the principles at small scale only.
It is falsified if
L loses its quality edge at larger sizes or when matrix-free
A fused GPU version gets within about 3x of the simulated chip
A transformer chip with the same memory matches its energy per token
Notes: This is the hypothesis, said as a hypothesis. A brain-style model with a constant-size state, sparse event-driven activity and low-bit weights, on a chip built for it, should need much less memory traffic and energy per token than a transformer on a GPU at the same quality. That could reduce the demand for scarce high-bandwidth memory and the heat and water of serving. The model has to be proven first, because the chip can only exploit those properties. It is falsified if the quality edge disappears at larger sizes or when matrix-free, if a fused GPU version gets within about three times of the simulated chip, or if a transformer chip with the same memory matches the energy per token. The thresholds are my proposals, not data.

## Slide 17: Where it is level, and where it is weaker
Nothing is measured on hardware yet: every chip number is simulated
Staged clothing about 82%, 5 points below its one pass; many ideas tried
A trained CNN is ahead by about 2 points on clothing when all data is available
Small tests: digits, clothing, 20 classes, up to 35 words; noise is simulated; two-sense data is paired by class
Second look costs about 2.8x memory; a few steps still run on the host
Notes: This is the slide I want you to remember. Nothing has run on hardware. Staged clothing is about 82 percent, five points under its one-pass number, and I tried many fixes. A trained CNN is still ahead on clothing by about two points. The tests are small and the noise is simulated; the two-sense data is paired by class, not real audio-visual recordings. The second look costs about 2.8 times the memory, and a few steps still run on the host.

## Slide 18: Not the first, and clear about what is new
Already exists
Hyperdimensional-computing accelerators
Intel Loihi 2, TrueNorth, SpiNNaker (event-driven spiking chips)
Replay-based continual learning
What we add
Dreams from 10-bit counters, no stored examples
A night that ends by itself; consolidation that scales with the data
No multiplier or matrix, bit-exact from raw senses to decision, with grouping and thresholds on the chip
Notes: We are not the first continual-learning chip. Hyperdimensional-computing accelerators and event-driven spiking chips such as Loihi 2, TrueNorth and SpiNNaker exist. What we add is the combination: dreams from small counters so no examples are stored, a night that ends by itself, consolidation that scales with the data, and a design with no multiplier or matrix that is bit-exact from raw senses to the decision.

## Slide 19: What comes next
1
Done
Model, RTL with every check passing, second look, tail memory, on-chip thresholds and grouping, scale tests
2
Next
Run on the real Tang Nano: the first MEASURED numbers
3
Then
Harder tests: larger vocabulary, real recorded noise, a harder image set
4
Later
Matrix-free chip for the L language model; ASIC memory for sound and the second look
Horizon: a provable result within 6 to 8 months, then shrink and attract investors. No fabrication is planned yet.
Notes: What comes next. The model and RTL are done and verified in simulation. The next milestone is the real Tang Nano board, which gives the first measured numbers. Then harder tests: a larger vocabulary, real recorded noise and a harder image set. Later, a matrix-free chip for the L language model, and external memory for sound and the second look. No fabrication is planned yet.

## Slide 20: Two tracks toward the bigger problem
Track 1: the L chip (hardware)
Now: verified in simulation, bit-exact RTL
Next: run on the Tang Nano for the first MEASURED numbers
Then: harder tests, external memory for sound and the second look
Track 2: the L AI model (later)
Gate 1: measure the model: firing rates, ablations, seeds
Gate 2: fused GPU baseline; stop if a GPU is already close
Gate 3: matrix-free version keeps its quality
Then: simulator and FPGA; study memory: can constant-size state and event-driven reads move work from scarce HBM to cheaper DRAM or SRAM? (a question, not a claim)
PLAN: the language-model track has small-scale evidence only (9M parameters).
Notes: We plan to approach the bigger problem on two tracks. Track one is the L chip, which is done in simulation and next goes to a real board. Track two is the L AI model for language, which has small-scale evidence only, so it goes through gates: first measure the model, then compare against a fused GPU implementation and stop if the GPU is already close, then check that a matrix-free version keeps its quality. Only then a simulator and an FPGA. Later we study memory: whether the constant-size state and event-driven reads can move work from scarce high-bandwidth memory to cheaper DRAM or on-chip memory. That is a question to study, not a claim.

## Slide 21: Silicon, node and size: the honest plan
Node
Who uses it / access
Cost, ESTIMATED
130 nm
open PDK (SKY130); prototype only, not comparable to a GPU
free flow; shuttle ~$10k-50k
28-65 nm
mature; via a university or Europractice-style programme
shuttle ~$50k-300k
5 nm class
today's data-centre GPUs (TSMC 4N, die up to ~814 mm2)
wafer ~$17k; design tens of $M
Material: silicon CMOS
The only practical choice for dense logic: mature, high yield, full tools. Limits: cost at advanced nodes, heat, SRAM not shrinking as fast, supply concentrated in few fabs. GaN, SiC, 2D materials and memristors are not ready for dense logic; non-volatile memory is a later option.
Plan: write the design node-agnostic; compare energy against GPUs at a GPU-class node using published scaling (ESTIMATED, uncertain); prove it on an FPGA; tape out at an accessible mature node when funded. A 5 nm-class chip needs tens of millions of dollars and foundry access we do not have: say so.
Notes: On fabrication. The open 130 nanometre flow is good for a prototype but not comparable to a GPU. Today's data-centre GPUs use a five-nanometre-class process and dies up to about 800 square millimetres. Reaching that node costs tens of millions of dollars and needs foundry access we do not have, so we will not claim it. The plan is to write the design independent of the node, compare energy against GPUs at a GPU-class node using published scaling, which is an uncertain estimate, prove the design on an FPGA, and tape out at an accessible mature node, around 28 to 65 nanometres through a university or shuttle programme, when funded. Silicon CMOS is the only practical material for dense logic: mature, high yield, full tools. Its limits are cost at advanced nodes, heat, SRAM that no longer shrinks as fast, and supply concentrated in a few fabs. Other materials are not ready for dense logic. All cost figures are estimates from memory of public reports; verify before quoting.

## Slide 22: What we need to go further
1
FPGA board run
Tang Nano 20K, about Rs 4,200 incl. GST (listing price + 18%, MODELLED)
Pass: bit-exact with simulation, accuracy and power measured
2
Micro-chip on a shared shuttle
about $100-300 per tile, 130 nm (ESTIMATED)
Pass: the verified on-chip units run in real silicon
3
Full chip at a mature node
shuttle $50k-300k, 28-65 nm (ESTIMATED), with a university or programme partner
Pass: measured energy within 2x of the FPGA-calibrated model
4
GPU-class node (5 nm class)
tens of millions of dollars: not requested now
Only after steps 1-3
Also welcome: a university or programme partner for shuttle access, a mentor, and compute credits for the language-model gates. Prices are estimates from public information: verify before committing.
Notes: What we need to go further, in steps, each with a pass criterion. Step one is the FPGA board run, about four thousand rupees including tax, and it gives the first measured numbers: bit-exact agreement with the simulation, accuracy and power. Step two is a micro-chip on a shared shuttle, around a hundred to three hundred dollars per tile, to show the verified on-chip units in real silicon. Step three is a full chip at a mature node through a university or programme partner, tens of thousands of dollars. Step four, a GPU-class node, costs tens of millions and is not requested now. Besides money we welcome a partner for shuttle access, a mentor, and compute credits for the language-model gates. All prices are estimates; verify before committing.

## Slide 23: A chip that keeps learning
It learns in the field, keeps what it knew, shares what it learned, and needs no multiplier. It is weaker than a trained network in some places, and we have said where.
Thank you. Questions?
Notes: To close: L is a chip design that keeps learning after it ships. It keeps what it knew, shares what it learned, and needs no multiplier. It is weaker than a trained network in a few places, and I have told you where. Thank you, I am happy to take questions.